## Slide 1
Aphrodite Kanellopoulou, George Zaraphonitis, NTUA
Yan Xing-Kaeding, Apostolos Papanikolaou, HSVA
Parametric design and Hydrodynamic optimization of a Battery-driven fast Catamaran vessel
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 2: Agenda
Project Outline
CAESES Parametric model
Potential flow calculations
Global Optimization
Conclusions
Surrogate Models
2
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 3: Project Outline
Parametric design & hydrodynamic optimization of a catamaran vessel, developed in the framework of the European R&D project TrAM (Transport: Advanced and Modular)
Objectives of TrAM project:
  To develop a series of zero emission fast passenger ferry designs
  To lower production cost by modular design
  To prove the viability of electric-powered high-speed vessels
    A prototype will be built during the project period and put into operation in Stavanger, Norway
3
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 4: Background information
Sketch of General Arrangement developed by Fjellstrand Shipyard in agreement with vessel operator
Main Dimensions:
  Length OA 31.0m
  Beam OA 9.0m
  Demihull Length OA 30.6m
Passengers: 147 (+20 bikes)
Route: Stavanger – Hommersåk
4
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 5: CAESES Parametric model
Set of Parameters
Grid definition
Lackenby Transformation
Surfaces Generation
Based on the background information, a parametric geometry model for the hullform was created by NTUA in CAESES
5
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 6: Definition Curves
FInterpolationCurve
Curve3DFrom2PlanarCurves
Interpolation Curve for section
definition
3D curves definition with feature Curve3DFrom2PlanarCurves
6
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 7
Surfaces
FLoftedSurface
FMetaSurface
Lofted Surfaces for Bow Area
definition
Meta Surfaces for Aft Part & Main Hullform definition
7
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 8: Hullform after Lackenby Transformation
After the hullform definition, a Lackenby transformation was used
Prismatic coefficient adjustment
longitudinal position of the centre of buoyancy adjustment
8
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 9: Main Global Parameters
  Waterline Length
9
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 10: Main Global Parameters
  Waterline Length
  Beam
10
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 11: Main Global Parameters
  Waterline Length
  Beam
  Draught
11
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 12: Main Local Parameters
  Transom width
12
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 13: Main Local Parameters
  Transom width
  Transom Chine Height
13
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 14: Main Local Parameters
  Transom width
  Transom Chine Height
  Shape of fwd profile
14
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 15: Potential Flow Calculations
-Shallo is a potential flow/ 3D panel method for the calculation of the wave resistance
The code estimates viscous resistance by empirical Method (ITTC), while considering
  accurate wetted surface
Accounts for the effect of transom sterns
Flow and wave pattern representation and pressure evaluation
Automatic re-panelling for each iteration
  Ship hull
  Αutomatic control of free surface mesh
Graphical User Interface
Background of HSVA in-house code
15
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 16: -SHALLO Integration into CAESES
 -SHALLO was the first of HSVA’s simulation tools with completed integration into the CAESES framework using the SoftwareConnector
Automatic hull form optimisation in Linux or Windows environment
16
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece
Geometry Panelization file
 -SHALLO input files
 -SHALLO result files

## Slide 17: Design of Experiments (DoE) for Stavanger Demonstrator using -SHALLO
Stavanger Demonstrator DoE | Description | Overall Beam of 9.0m
(Global) Design Variables for demihull | LWL | 29~30.2m
 | Beam | 2~2.6m
 | Initial Draught | 1.2~1.6m
 | Transom width | 0.8~0.85
Design Conditions | Weights | Δ1, Δ2, Δ3
 | Ship Speed | 21, 23, 25 kn
Design Constraints | Battery space | 1634x2029mm
Design Results | No. of calculations | 1800
Evaluated Variables |  | RT
 |  | Sinkage/Trim
17
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece
Vs=21kn Vs=23kn Vs=25kn
-SHALLO indicative results for a hullform design variant

## Slide 18: Use of Surrogate Models instead of Direct Calculations for Reduced Computational Time
Various surrogate models were generated and tested for calm water resistance calculation based on -Shallo results.
Most accurate and fast method: MARS (Multivariate Adaptive Regression Splines) (error ≤ ±0.5%).
Surrogate models replaced direct calculations by CFD tools in optimization studies.
Δ3 Displacement at 21kn
Δ2 Displacement at 21kn
18
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 19: Global Optimization Studies
Global optimization studies performed using NSGA-II genetic algorithm
Objective of the study: to minimize calm water resistance of the bare hull
To obtain hullform with superior characteristics in a range of displacements & speeds, the following weighted objective function is used:
Constraints:
  Minimum demihull width & height for installation of batteries
  Height of tunnel at centreline for propeller installation
19
RT = 0.12RT_21kn, Δ1 + 0.20RT_23kn, Δ1 + 0.08RT_25kn, Δ1 +
0.09RT_21kn, Δ2 + 0.15RT_23kn, Δ2 + 0.06RT_25kn, Δ2 +
0.09RT_21kn, Δ3 + 0.15RT_23kn, Δ3 + 0.06RT_25kn, Δ3
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 20: Design Variables
According to the 1st Design Scenario:
  catamaran’s length overall fixed at 31.0m
  beam overall fixed at 9.0m
Design variables considered:
  Waterline Length
  Demihull’s Beam
  Initial Draught
  Transom width
20
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 21: Global Optimization Results
Displacement: Δ1
Vs=21kn Vs=23kn Vs=25kn
21
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece
Total Designs Produced: 1000
  824 Feasible
  176 Unfeasible

## Slide 22: Global Optimization Results
Displacement: Δ2
Vs=21kn Vs=23kn Vs=25kn
22
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece
Total Designs Produced: 1000
  824 Feasible
  176 Unfeasible

## Slide 23: Global Optimization Results
Displacement: Δ3
Vs=21kn Vs=23kn Vs=25kn
23
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece
Total Designs Produced: 1000
  824 Feasible
  176 Unfeasible

## Slide 24: Optimum Design Selection
  Based on hydrodynamic characteristics and construction/maintenance issues, an overall optimum design was selected
24
 | at Δ1 | at Δ2 | at Δ3
LWL | 29.29 | 29.34 | 29.39
Beam at WL | 2.442 | 2.442 | 2.444
Draft | 1.226 | 1.272 | 1.317
Rt_21 kn /Δ | 0.558 | 0.599 | 0.642
Rt_23 kn /Δ | 0.588 | 0.620 | 0.663
Rt_25 kn /Δ | 0.658 | 0.684 | 0.717
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 25: Conclusions & Next Steps
  Parametric model for fast catamaran design developed by NTUA in CAESES, integrated with HSVA’s -Shallo
  Development of surrogate models for calm water resistance on the basis of CFD results
  Multi-objective Optimization studies using NSGA-II genetic algorithm
  Conducted global optimization studies show that:
    Demihull hullforms with smaller beam have lower calm water resistance for lightest displacements
    At higher speeds and displacements, beamier hullforms are performing better
  Based on hydrodynamic characteristics and construction/maintenance issues an overall optimum was selected for more refined optimisation
  Local hullform optimization for improved resistance and propulsion characteristics are currently in progress using HSVA’s CFD viscous flow RANS solver FreSCo+
  The resulting hullform will be tank-tested by HSVA and used for building of the Stavanger prototype
25
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece

## Slide 26
Sustainable and Safe Passenger Ships, 4th March 2020, Athens, Greece
Thank you for your attention
Parametric design and Hydrodynamic optimization of a Battery-driven fast Catamaran vessel
Aphrodite Kanellopoulou, George Zaraphonitis, NTUA
Yan Xing-Kaeding, Apostolos Papanikolaou, HSVA